Kurt Robertson  MAZDA               503-829-6054Kurt Robertson’s  ROTARY  ENGINES

OWNER  BREAK-IN  AND  SERVICE  PROCEDURES

IMPORTANT  WARRANTY  INFORMATION:

Thank you for purchasing a REII Remanufactured Engine.

Your engine has been carefully remanufactured to factory tolerances to ensure good performance and long life. In order to protect your investment, please read and follow these Guide-lines. The first few thousand miles of service are the most critical in the life of your REII Remanufactured Rotary Engine.                Our warrantee covers all engines.

Stock engines coverage includes 100% Parts and 100% Rebuild Labor with required service documentation during first 12 months / 12,000 miles

OWNER/DRIVER’S RESPONSIBILITY

FAILURE TO  OBSERVE THE PROEDURES THAT FOLLOW MAY VOID YOUR WARRANTY.

While operating the smooth and low vibration rotary engine the driver must be on the lookout for signs of malfunction. By responding correctly to the first indications of trouble with your rotary engine you can keep your warranty in force and avoid a costly repair.

1.   OVERHEATING - Indicated by “Temp” or “Engine” light

lighting , or Temperature Gauge reading above normal range.

A. STOP THE CAR IMMEDIATELY. Failure to do so will

lead to serious overheating and engine damage.

Rotary engines are very sensitive to heat, warranty is

void when overheating is due to belt, hoses, radiator, water pump, or

other cooling system related failure.

2.   OIL STARVATION - Indicated by “Oil” or “Engine” light

or oil pressure gauge indicating low pressure. Engine over-

heating , engine knocking and poor performance are other

warning signs.

A.  STOP THE CAR IMMEDIATELY. Check the oil level in the

crankcase and bring it up to full mark on dipstick.

B.   If condition persists, seek help from your certified mechanic

as soon as possible to determine cause (low oil level, oil leaks, oil

Cooler, low oil pressure, etc.)

C.     Do not continue to operate the vehicle until

the oiling system is fully operational.

Conclusion:

If you diligently change your oil and keep a clean cooling system you can increase the life of your REII Remanufactured

Engine.  Conversely, your warranty will be void if the failure is caused by the OWNER/DRIVER RESPONSIBILITES as described within this booklet.

-------------------------------------------------------------------------------

BREAK - IN  PROCEDURES  FOR  YOUR  NEW  REII  ENGINE

FIRST 500 MILES

Drive normally, but not at continuous high RPM (6,000-7,000) for the first 500 miles. “ A redline a day -keeps the carbon away”

Avoid “lugging” the engine, towing a trailer (REPU), or overloading the vehicle.

Check engine light, if set, indicates an emissions control problem and a flashing light will indicate a misfire, do not be alarmed if light has illuminated during break in or before the first 3000 miles.

Check the Oil level and Coolant level frequently, and fill as needed. CAUTION: Follow car manufacturer’s procedures when performing these functions.   NOTE*  Newly rebuilt engines frequently consume excess oil for several hundred miles. This should not be cause for alarm unless the condition persists. Don’t be alarmed if fuel economy is disappointing at first. New engines often yield better mileage after break in, have the ignition and fuel systems checked and adjusted  (if adjustable) at 3000 miles.

WRITTEN WARRANTEE  Peter  11/6/19   100,000 miles

All Engines guaranteed to be defect free for a minimum of 12 months/12,000 miles, user is responsible for failures due to oil starvation, overheating, lack of oil  or bad radiator condition.  See Kurtrobertsonenterprises.com for complete warrantee information and warrantee book. Required service is to be completed every 3000 + 100 miles- Unless Noted Otherwise

1000 MILE SERVICE-  Change Oil and Filter, check all hi pressure oil and water fittings, check chassis for leaks , adjust timing and idle speed and address any issues as noted by customer

Kurt Robertson Mazda    101,050 Miles____                          __ Date               Signature

3000 MILE SERVICE- Change oil and filter, check chassis as above , repairs as necessary

Kurt Robertson Mazda     103,050 Miles                             _  ___ Date                  Signature

6000 MILE SERVICE- Change oil and filter, check chassis as above , repairs as necessary

Kurt Robertson Mazda     106,050 Miles_                                _ ___ Date              Signature

9,000 MILE SERVICE- Change oil and filter, check chassis as above , repairs as necessary

Kurt Robertson Mazda     109,050 Miles                                              Date            Signature

KURT ROBERTSON MAZDA 503-829-6054