USEFUL FORMULA FOR CALCULATING ENGINE PERFORMANCE

RICHARD A. PAUL

5/6/01

FIND THE MASS OF INTAKE CHARGE:

CFM X MAN PRSS ABS X AMB TEMP R X .076

29.92 X MAN TEMP R

= LBS.  AIR PER MIN.

NOTE: .076 IS STANDARD CORRECTED DRY AIR, 60 DEGREES F AT SEA LEVEL

-------------------------------------------------------------------------------------------

FIND THE AREA OF INTAKE FOR GIVEN AIRSPEED AND CFM

A=

CFM

60

FPS

FIND CFM WITH AIR SPEED AND AREA

AREA X FPS X 60= CFM

THIS IS CFM NOT MASS YOU MUST KNOW DENSITY TO GET LBS./MIN

--------------------------------------------------------------------------------------------

TEMP RISE FOR GIVEN SUPERCHARGE AND EFFICIENCY

R= Y x T RENKIN    (AMBIENT ABSOLUTE)

Y=Pr to the power of .283-1

This is for 100% eff    divide by compressor efficiency for actual discharge temp

HP TO MAINTAIN A GIVEN SPEED

CD X FRONTAL AREA X (MPH TO THE CUBE)

146,600

THIS IS TO MAINTAIN SPEED NOT TO ACCELERATE TO IT.

ADD 15% FOR DRIVE LINE LOSS (STD TWO WHEEL.)

ADD FOR ALTITUDE

HOW MUCH TO ADD FOR ACCELERATION DEPENDS ON HOW LONG THE COURSE IS.

IF YOUR RUNNING AT BONNIVILLE ADD 15% FOR ALTITUDE LOSS.