2005 - RX8 - Workshop Manual - Engine

10 LOW IDLE/STALLS DURING DECELERATION

*DESCRIPTION*

* The engine stops unexpectedly at the beginning of deceleration

or recovery from deceleration.

*POSSIBLE CAUSE*

* Vacuum leakage

* Air leakage from intake-air system

* Air suction at intake-air system (between MAF sensor and

intake part)

* Improper operation of drive-by-wire control system (abnormal

accelerator position and TP signals to PCM)

* Drive-by-wire control system operates in fail-safe mode

(abnormal accelerator position and TP signal to PCM)

* Throttle body malfunction (restriction, stuck closed)

* Evaporative emission control system malfunction

* Improper operation of fuel cut control

* Fuel injector improper operation

* Fuel injector malfunction (leakage, clogging, improper

injection amount)

* Inadequate fuel pressure

* Pressure regulator (integrated in fuel pump unit)

* Fuel pump mechanical malfunction

* Fuel line restriction or clogging

* MAF sensor improper installation

* MAF sensor or related circuit malfunction (abnormal signal to PCM)

* Brake switch or related circuit malfunction (abnormal signal

to PCM)

* Neutral/CPP switch or related circuit malfunction (abnormal

signal to PCM)

* TR switch or related circuit malfunction (abnormal signal to PCM)

* Low engine compression

o Engine internal malfunction

o Abnormal engine oil condition (viscosity, deterioration)

o Low oil pressure

o Excessive fuel pressure

o Air mixed in oil line

o Metering oil pump malfunction

+ Leakage or clogging in oil pipe

+ Leakage or clogging in oil nozzle

* Improper A/C magnetic clutch malfunction

* Misfire

* Improper operation of torque converter clutch control (AT)

* Loose installation of engine mounts